## Slide 1: JASTER Instruction (Jason Altimetry Stand-Alone Tool for Enhanced Research)
Amirhossein Rostami, Natalya Maslennikova, Hyongki Lee
Department of Civil and Environmental Engineering
University of Houston

## Slide 2: Outline
Python setup
Some preparations before running JASTER
Run JASTER
Example results

## Slide 3: Python Setup 1. Install Anaconda
Anaconda
  Create virtual environment for better management of python packages
  Download and install
    Link: https://www.anaconda.com/download

## Slide 4: Python Setup 1. Install Anaconda
Miniconda
  If you do not have anaconda installed, we recommend using Miniconda,
  Download and install
    Link: https://docs.conda.io/projects/miniconda/en/latest/

## Slide 5: Python Setup 2. Create a virtual environment
Run “Anaconda Prompt” in Windows or open the terminal (on macOS or Linux)
In “Anaconda Prompt,” enter:
  conda create --name NAME_OF_ENVIRONMENT (we suggest naming it jaster_env for convenience)

## Slide 6: Python Setup 2. Create a virtual environment
Run “Anaconda Prompt” in Windows or open the terminal (on macOS or Linux)
In “Anaconda Prompt,” enter:
  conda create --name NAME_OF_ENVIRONMENT (we suggest naming it jaster_env for convenience)
  Enter “y” when being asked “Proceed ([y]/n)?”
  Wait till installation complete

## Slide 7: Python Setup 2. Create a virtual environment
Run “Anaconda Prompt”
In “Anaconda Prompt,” enter
  conda create --name NAME_OF_ENVIRONMENT (e.g., jaster_env)
  Enter “y” when being asked “Proceed ([y]/n)?”
  Wait till installation complete
Activate the virtual environment

## Slide 8: Python Setup 3. Install required packages
Required Python Modules: netcdf4/numpy/matplotlib/scipy/matplotlib/ etc.
  Install by typing in (make sure you have activated the virtual environment)
    conda install python pip matplotlib numpy scipy requests
    conda install -c conda-forge gdal
    conda install tkinter (If you get error, then use “conda install anaconda::tk”)
    pip install netcdf4 rioxarray rasterio screeninfo
    pip install -U scikit-learn
    pip install hampel
      You may get error while installing hampel package (It is more likely to happen for Windows users)
(1)
(2)

## Slide 9: Python Setup 3. Install required packages (Cont.)
In this case, If you don't have the Microsoft Visual C++ 14 version or greater,
  go to the (https://visualstudio.microsoft.com/visual-cpp-build-tools/ )
  download Microsoft C++ Build Tools.
  install Visual Studio (most updated version is preferred) and also Windows SDK (11 or 10 based on user's windows version).

## Slide 10: Before Running JASTER
  To download Jason series altimetry data:
        Create Account via AVISO: https://www.aviso.altimetry.fr/en/my-aviso-plus.html

## Slide 11: Before Running JASTER
  OpenTopography API Key
      To achieve the SRTM DEM API Key,
      go to the https://portal.opentopography.org/login and create an account if you do not have:

## Slide 12: Before Running JASTER
Check pass # using Google Earth and Jason ground track (Visu_RefOrbit_J3J2J1TP_Tracks_GoogleEarth_V3.kmz)
  Download kmz via: https://www.aviso.altimetry.fr/en/data/tools/pass-locator.html
Pass #
Latitude Range: 32.811~32.823

## Slide 13: Before Running JASTER
Open Anaconda prompt and change working directory to where the python codes exist:
  By default, working directory is in C drive. To switch to other drive:
  cd ‘PATH_TO_YOUR_PYTHON_CODE’
  ‘geoidegm2008grid.mat’ and Water Occurrence maps are required for time series plot.
  Then, execute “python JASTER.py” launching JASTER and opens its graphical user interface.

## Slide 14: Before Running JASTER
You may encounter some errors before running JASTER such as:
  No module named “name of the module” even though you have already installed it. For example:
  In this case, reinstall modules which give this error in Anaconda Prompt as we described in slide 8
  If it does not work again, reinstall modules through Jupyter Notebook

## Slide 15: JASTER Inputs
  Input all required information
    AVISO username & Password (slide 10)
    API Key to download SRTM DEM from OpenTopography (slide 11)
    Jason Series #: select 2 or 3 or both
    Pass #: from 1 to 254
    Start and end cycle #:
      Jason-2: Cycle ranges from 1 (2008/07) to 303 (2016/09)
      Jason-3: Cycle ranges from 1 (2016/02) to most recent 226 (2022/03) (Replaced by Sentinel-6 afterward)
    Latitude and Longitude range of the reservoir/lake of interest from Google Earth (slide 12)
    Height and WO threshold for SRTM DEM-WO deoutlier method
    Hampel filter parameters (W, S). If you don’t want use Hampel, let Window size = 0
    Directory path to save JASTER output results
1

## Slide 16: Data Download
  Open “j2_Pass#” or “j3_Pass#” folder after data download complete to confirm the downloaded cycles
2
3

## Slide 17: Variable Extraction
Extraction Processing
When it becomes completed
Jason-2
Jason-3
4
5

## Slide 18: Variable Extraction
Columns:
(10) Jason-2 or 3 Cycle Numbers
(11) Decimal year
(12) Longitude
(13) Latitude
(14) Height (meter w.r.t. EGM2008 Geoid) before applying outlier removal methods
(15) Uncertainty (meter)

## Slide 19: SRTM DEM-Water Occurrence outlier removal
We have already provided users with WO maps in JASTER data file.
Users can also download it directly from (https://global-surface-water.appspot.com/download )
API key of OpenTopography + (Lat, Long) range.
SRTM DEM will be downloaded automatically.
WO map and SRTM DEM are cropped based on Lat and Long range that user defined for the area of interest.
6
7

## Slide 20: Time Series Plot (Final Outputs)
These are all JASTER output files with corresponding time series plots:
Jason-2 IQR
Jason-2 SRTM DEM-WO
Jason-3 IQR
Jason-3 SRTM DEM-WO
8
9

## Slide 21: Time Series Plot (Example: Hubbard Creek Lake, TX)
All JASTER output results for Hubbard Creek Lake including: Jason-2 and 3, IQR and SRTM DEM-WO, enabled and disabled Hampel filter.
Water elevation w.r.t EGM08 Geoid
Columns:
(1) Jason-2 (or 3) Cycle Numbers
(2) Water Height (meter w.r.t. EGM2008 Geoid) without Hampel filter
(3) Uncertainty (meter)
(4) Decimal year
(5) Water Height (meter w.r.t. EGM2008 Geoid) with Hampel filter

## Slide 22: Acknowledgment
NASA’s Water Resources Program (80NSSC22K0918)
SERVIR Program (80NSSC23K0184).
Contact: Hyongki Lee at hlee45@central.uh.edu